Flaming pyrolysis modelling and development of the long stick wood gasification in a truncated updraft gasifier

A. Saravanakumar*,  T.M. Haridasan, Thomas B. Reedb

a NSP Green Energy Technologies Private Limited, Renewable Energy Research and Development, Flat No. 3, Mahaguru Apartment, Elim Nagar, 1st Main Road, Perungudi, Chennai - 600 096, Tamil Nadu, India.

bThe Biomass Energy Foundation, 554 Orchard Street, Golden, CO 80401, USA

Abstract

The long stick wood gasification process was studied at transient state conditions in a pilot scale fixed bed truncated updraft system. The present work is therefore focused on long stick wood as a feed material to the gasifiers. This truncated updraft mode operates with 180W of blower supply for air to produce 10kW thermal output. Results were obtained for various flow conditions with air flow rates ranging from 20 to 30 m3/hr. For modelling, the flaming pyrolysis time for long stick wood in the gasifier is calculated to be 1.6 min. The length of the flaming pyrolysis zone and char gasification zone is found to be 34cm and 30cm respectively. The rate of feed was between 9 to 10 kg/hr and continuous operation for 5 hours was made in a thrice of runs to study the performance. The truncated updraft mode makes it possible to produce low tar content in producer gas.

Key words: Flaming pyrolysis model; Truncated updraft gasification; Long stick wood

* Corresponding author, Tel.: + 91-9176686944

E-mail address: sara_mnes@yahoo.co.in (A. Saravanakumar)

1. Introduction

Wood was the primary energy source for cooking, heating and metals production from the opening of recorded history until the time of the industrial revolution. At the end of the middle ages, wood was used across India in smelters producing iron, copper, lead, and other materials. Industrialization continued and demand growth for these products. The demand for wood exceeded availability, causing the shutdown of many smelters, shortages of wood for cooking and deforestation. Woody biomass is considered the renewable energy source with the highest potential to contribute to the energy needs of modern society for both the developed and developing economies world-wide (European Commission [1] and International Energy Agency [2]). Woodchips is one of the sources of biomass renewable energy that can produce gas from gasification. It has the greatest potential of any renewable energy option for base-load electric power production for electricity generator and heating. High penetration of biomass technologies shall require abundant supply of biomass resources. Wood shavings in fine form from wood process industries and agricultural wastes have also been used to augment the supply of heat both in domestic and industrial situations. Hislop and Hall [3] reported that the third world where the availability of industrial electricity is seen as a key factor in assisting development in rural areas, gasification can provide a local source of electricity using local woody biomass.

The primary research in wood gasification for many years was has been in the area of design and performance aspects of gasifier, where tar minimization has been the primary concern. The issues of feedstock preparation for wood as an energy source were of meager interest. As a result, research in coal gasification has progressed much further than research in wood gasification. Even the use of long stick wood for gasification is unique in that there is a wide range of fuel sizes and moisture contents. Wood based gasifier improvement has come to a quite experienced state after one assures steady supply of wood chips in the required dimensions. While serious efforts have gone in the design of the gasifier for generating optimum gas yield along with similar efforts for cooling and cleaning. The major problem of the handling and preparation of input in the form of wood chips remains still as a noticeable stumbling block in the penetration of this technology both in industries and in the domestic sectors. This situation is more serious if we have to put gasifier systems in remote rural areas where they are really needed. However, these are the regions mostly suffering from power shortage or absence of power itself. However, such power is initially needed for blower operations and many a time also for woodcutting. Feed stock preparation is thus an important aspect of the complete systems planning and such preparation typically involves cutting wood into required size. Electrical power, manpower, and storing facility involved in such processes make the functioning cumbersome especially in an industrial area. The chip size recommended by the manufacturers of gasifier feed system must be ascertained before obtaining wood chips from a supplier, or before acquiring any chipping or shredding equipment. Miles [4] reports the International Energy Agency Biomass Thermal Gasification

Activity has reported the gasification technology is faced with the constraints of feed preparation for wood based systems and the need of special designs for loose biomass as feed.

As per our experience, cutting of wood involves sizable amount (above 10% and up to 15%) of wood wasted as dust. Saw cutting alone generates 10% sawdust on weight basis. Where cost of wood is high, this wastage will be a major cost addition. For example, if a ton of wood costs around US $26 as now prevalent in India then the wastage costs at least is around US $3 per ton. Additional cost caused by loss of moisture from 30% to 15% (and hence reduction in weight) of the wood will result if the fuel is left to dry for just a few days, after cutting into small pieces. This further adds on to the cost. Wood chips suitable for medium size gasifier reactors are made available now by manual cutting. Mechanical cutter, electrical cutter, briquettes and charcoaling can control the dimensions. However, the above methods in preparation of wood chips have the disadvantages such as consumption of electricity, high manpower needs, dust collection, enormous noise production and occasional unexpected accidents during processing. Therefore, it is not possible to process and store the wood for a long period. Hence, to reduce the above-mentioned problems we have to focus on the long stick as feed material in the gasifier. In the spirit of using energy plantation for such gasifier system, it is preferred to use the stock with this branches which can be replenished in the plantation site in shorter time span as compared to big trees being cut.

2. Long stick wood as feedstock technology reliability

Clean biomass feedstock are becoming scarce and there is hardly any reliable supply. In India, all industrial wood waste and other wood residues are consumed completely and there is no other clean biomass available to increase the contribution of bio energy. Thus, the industry has been obliged to look into relative difficult fuels and fuels with little practical industrial experience in order to create new market opportunities. Waste recovered fuels present the advantage that they often have a negative cost associated with their disposal, which can significantly decrease the operating costs of a plant. In addition, since the last decade there has been a significant interest in energy crops and especially short rotation forestry (SRF) as a means to increase the production of biomass fuels while simultaneously creating new jobs for the farming community.

Helynen et al. [5] shows woody biomass has the highest reliability in feeding into a gasifier and most problems related to bed sintering in fluidized bed gasifiers or slag formation on heat exchange surfaces are relative well understood. The industry has sufficient confidence to use effectively most types of woody biomass. The industry has also attained a high degree of reliability for the pre-treatment operations such as drying, size reduction and storage. The market potential of woody biomass is boundless as most of the locally available feedstock are highly consumed in various industrial or district heat applications. Saravanakumar and Haridasan [6] have studied that the wood logs could be cracked at temperature range of about 275-325˙C. The ratio of volume loss of wood per second to volume of the wood used in combustion was found to be 0.0015 1/s indicating the long-range feasibility of adopting long sticks as feed. From this experiment, they have also learnt that controlled cracking of wood is  desirable strategy. The loss of wood in the process is negligible. The time for fuel wood preparation is short. Controlled handling of bigger logs in a closed reactor may have to be addressed.

3. Design of truncated updraft gasifier

Based on the ideas observed from the preliminary work, a long stick wood gasifier for truncated updraft mode was constructed. It was designed and constructed using mild steel sheet with 4.3mm thickness with a volume is 0.714m3. The total height of the gasifier is 1.34m. Hopper is the primary storage area for the fuel wood. Feed stock size for long stick wood of length 68cm and thickness of 6cm is placed into the top of the hopper through the inlet. The hopper is designed in such a way that it is able to hold wood, which can produce the gas continuously for 5 to 6 hours. Initially, charcoal pieces are first loaded up to air nozzle height. Then long stick wood is packed up to the full capacity of the hopper. Hearth is made up of castable cement with a mild steel exterior cladding to encounter higher temperature up to 1600º C. Cuda and Ziak [7] fabricated the cross-draft gasifier, though used only with charcoal feed stock, has operating temperatures in excess of 1500ºC. The air from the blower for partial combustion enters the hearth through air nozzle. The air nozzle tube is made up of SS material 1.5-inch diameter. There are two air nozzles fixed with adjacent side of the hearth. It is shown in Fig. 1. The positioning of the grate below the hearth zone in the gasifier is to help the reduction reactions. The grate directly supports the combustion zone and must be capable of letting ash fall through without an excessive loss of fuel. In addition, the grate is used to control reactor pressure drop and hence to maintain the gas production rate.

4. Performance of truncated updraft gasifier

Bryden and Ragland [8] have studied the whole tree by utilizing a deep, fixed bed combustor/gasifier. This wood logs 20 cm in diameter is smouldered in a 3.7 m deep fuel bed. In this work we have operated the truncated updraft mode attaining high energy release rate per unit area due to high inlet air velocity and activated reaction in combustion zone. Reed and Ronal Larson [9] have developed a top lit updraft gasifier using the fuel wood size 1-3 cm softwood chips, 1-2 X 10 cm hardwood sticks and 5 mm. They used the long stick size is 2 X 1 X ½ cm. It is placed vertically. Saravanakumar et al. [10, 11] used transient state conventional updraft gasifier with packed bed for long stick wood of length 68cm and thickness of 6cm. In conventional updraft gasifiers operated charcoal is burned to produce hot gases above 1000°C that then successively pyrolyse and then dry the full bed of fuel. They suffer from a continuously changing gas stream as the whole charge is first dried and then pyrolysed to charcoal which is then burned. We have constructed a “Truncated updraft Gasifier” in which burning charcoal provides hot gas to dry and pyrolyse the incoming fuel in a short section and then exits. Fresh fuel flows continuously to the top of this layer. The gasifier system was run ten times, each for a period of 5 hours and 15 minutes in the truncated updraft configuration. Among these runs, three runs have been selected and discussed. For the feed Azadirachta Species was utilized and the time needed for the gas to support combustion from the initial flaring was 10 minutes. The total wood consumption in the run was 45kg. The performance details are given in the Table 1. The air/fuel ratio increases from 1.3 to 1.7 as more and more of the charcoal are gasified and the process approaches complete combustion. The results of operation of truncated updraft and conventional updraft gasifier runs 1, 2 and 3 are given in Table 2. The truncated updraft gasifier is found to have a more calorific value of the producer gas at 4.3 MJ/m3 with the resulting average efficiency of 79% as against 67% for the conventional updraft gasifier. The truncated updraft gasifier produces 1–0.3% tars as indicated in Table 2 as against the conventional updraft gasifier used in the present study with 10–30% tars. Many gasifier designs produce so much tar that the gas cleanup equipment cost is several times the gasifier cost. Fluidized beds typically produce 0.5–4% tars while conventional updraft biomass gasifiers produce 10% tars. From the overall point of performance of the gasifier, the truncated updraft mode is found to have a more satisfactory performance.

5. Flaming pyrolysis time – Modelling of truncated updraft gasifier

Ten kilogram of charcoal is placed on a grate and is ignited by two fire ports. It appears that the blower is run in suction mode to draw air in through the fire ports during the charcoal ignition. 60 kg of long stick wood is placed on top of the charcoal. The fire ports are closed and the supplied flame through the two fire ports stops. The fan is run in blower mode and the air enters from below the bed. The primary air for pyrolytic gasification enters at the bottom and moves up, forming gas in the flaming pyrolysis zone as shown in Fig.2. This airflow is measured by pressure drop across a restriction. Gases produced by the wood and charcoal exits through a gas port. This gas is combusted and the gas flow rate (via pressure difference) and the producer gas flame temperature are recorded. Drying, pyrolysis, and Combustion of the packed bed continue until the flame at the gas port goes out. We have examined the quantity and the nature of the ash collected after the different performance trials. As expected, the quantity of ash collected with the truncated updraft mode is smaller compared with that of the conventional updraft mode. The quality of the gas also is better due to the cracking of tar in the truncated updraft mode.

In modelling the flaming pyrolysis zone of the gasifier it is essential to know the amount of time and energy that is required for pyrolysis. The heat transfer to each long stick wood particle in the flaming pyrolysis bed is by conduction down from the charcoal layer to the combustion interface to the surface; by convection from the gases streaming outside the long stick wood particle boundary layer; and by radiation from other wood particles, from the reactor walls, and by the luminous flame. Updraft gasifiers consume the tars by a process we call flaming pyrolysis [12]. The combustion of pyrolysis products in an air in sufficient supply (as in a match) is termed ‘‘flaming combustion’’. We apply the term ‘‘flaming pyrolysis’’ to the combustion of the same volatiles in an inadequate supply of air so that the products are largely CO and H2 rather than CO2 and H2O. In flaming combustion the heat for pyrolysis is provided by combustion of the pyrolysis products and radiation from adjacent particles or a surrounding combustion zone. This heat must be transferred to the particle surface through the flaming pyrolysis wind as shown in Fig.2. This process is self-adjusting in part. Any factor that increases heat transfer also increases the rate of streaming and the thickness of the boundary layer. This is in turn tends to reduce the heat transferred by convection across the boundary layer. Based on the Reed et al. [13] equation, the time required for flaming pyrolysis of a wood particle, tfp is given by

tfp = 0.207 ρFs (1+1.76Fm) D (1+ 0.61D) exp(4369/RT) / (1+ 3.46Fo2) (1)

The time for flaming pyrolysis equation dependent on particle size, shape, density etc. to describe in a fixed bed. This equation is used for the maximum size of the wood stick are 4.5cm x 0.7cm x 0.57cm for the small size woody biomass material. The times predicted could be highest because long stick wood length or height is important part of the heat transferred and the heat is utilized during the flaming pyrolysis process. In order to account for this we have to modify the tf p equation to include the denominator using the long stick wood density, sphericity and height. Therefore flaming pyrolysis time for long stick wood is given below.

tfp = 0.207 (1+1.76Fm) D (1+ 0.61D) exp (4369/RT) / (1+ 3.46Fo2) ρFs L (2)

tfp = 1.6 min

Where tfp is the time (in min) required for flaming pyrolysis of a long stick wood of density

ρ = 0.5g / cm3, average dimension D = 12cm (equal to the cube root of the volume, V1/3),

sphericity Fs = 1.8 and moisture content Fm = 0.20 (dry basis). R is the gas constant =1.98, Fo2 is the initial fraction of oxygen in the ambient air and T (K) is the pyrolysis zone temperature (850°C) for the gasifier. Table 3 represents the large numbers of variables used for this following equation.

Note that in this equation those terms that involves the mass of the wood, density, moisture content and increased time for pyrolysis in a linear mode. The dependence of time on length of the wood, D. is also linear for large wood particles where D > >1. The dependence becomes quadratic for D>1 where the resistance to heat flows depends on heat flow resistance in the wood as well as in the gas boundary layer. We have estimated the velocity of motion of fuel in the gasifier as a function of the amount of wood being gasified and it is found to be 0.3cm/sec

Vf = M / Ag Fd (1-Fv) (3)

The length of the flaming pyrolysis zone Lfp, is found to be 65cm.

Lfp = Vf x tfp = 34.2 cm (4)

We take combustion time tc arbitrarily to be 100 sec.

The length of the charcoal gasification zone is

Lc = Vf x tc = 30cm (5)

6. Results and discussions

6.1 Validation of gasifier conditions for the measured data

In the experience of long-stick wood gasification, such a model is very critical when compared to the cases of wood particles, pellets, and char, etc. The temperature at a location rises first in the combustion zone and then rises smoothly through the pyrolysis and drying zones. When the wood is completely charred, the temperature increases. In the pyrolysis section steady state, temperature ranges between that of the hot combustion surfaces and that of the cold unreacted core. The temperature was measured as a function of time at 15 min intervals at the layers from the bottom to the top surface of the gasifier. The temperature ranges from 1185K in the combustion zone to 400K in the drying zone. We have found the gasifier conditions at different size of wood 68x6cm and flaming pyrolysis temperature ranges from 850°C to 1000°C. The equations 2, 3, 4 and 5 tested by estimating the pyrolysis time, fuel velocity and length of reaction zone has excellent fit for the theoretical and practical results. The different conditions for gasifier results are as shown in table 4.

6.2 Results on velocity of fuel flow in the gasifier

Saastamoinen [14] has studied on the modelling of wood gasification in conventional updraft mode. In this, gasifier was operated by lowering the air rate beyond a critical value increasing the bed height without a limit. We have operated the truncated updraft mode based on high- energy release rate per unit area due to high inlet air velocity and activated reaction in combustion zone. If long stick wood is added on top of the burning charcoal, it will be pyrolyzed by the heat, giving a mixture of gases and volatile condensable compounds. As they are generated, the charcoal is replenished, so that a steady state can be reached by adjusting the rate of wood feed. We have estimated the velocity of motion of fuel in the gasifier as a function of the amount of wood being gasified and it is found to be 0.3cm/sec (after Reed et al. [13]. In our experience, truncated updraft gasifier is found to be suitable for long stick woody biomass materials with high inlet air velocity.

6.3 Effects of temperature at different zones on the gasifier

With the gasifier long stick wood was tested for different airflow rates of 25,35,38,45, 50 and 53 m3/hr. Temperature profile on different zones as a function of airflow rate is shown in Fig 3. The graph indicates the high-energy release rate per unit area due to high inlet air velocity and activated reaction in combustion zone. When the air is directly getting in to the combustion zone, high temperature is achieved.

6.4 Effects of air velocity and gas flow rates on the gasifier

The Fig 4 shows gas production rate increasing with increase of inlet air velocity with linearity and steadier gas production up to an air velocity of 1.96m/sec. The inlet air velocity ranges from 2.25 to 2.64 m/sec increasing gas production largely. It is obvious that the gas production rate would show a similar behaviour with the change in airflow rate. We have estimated the air velocity of motion of inlet air in the gasifier

Air velocity = Airflow rate / Area of the flow pipe

= 0.0051m3/sec / 0.0031m2 = 1.64m/sec

6.5. Effect of model with observed gasifier conditions

Measurements of flaming pyrolysis time, active zone length and temperature were made at the grate of the 529 cm2 area long stick wood gasifier, operating with long stick wood size (cylindrical) of 68 cm x 6 cm as a function of the top of the flaming pyrolysis zone above the grate. The calculations are shown in table 3 and 4 graphically to scale with a schematic diagram as shown in Fig 5.

7. Conclusions

Truncated updraft long stick wood gasification technologies have reached the point where the first simple applications with minimal technical risks are becoming commercial. The development of the technology has moved beyond the element of the “gasifier” to the critical area of the supply of a “clean gas,” free of particulates and tar. If this will be achieved, then the power market will be slowly but steadily penetrated on condition that sufficient feed stocks can be secured. The experience of gasifier users with regard to the effort and energy needed for wood chip preparation in a typical gasifier has led us to the development of a gasifier suitable to work with long-stick woody biomass as the feed material. In the spirit of using an energy plantation for such a gasifier system, it is preferable to obtain such sticks from the branches of trees, which can be replenished at the plantation site in a shorter time span as compared to big trees being cut.

For the modelling, the gasifier was divided into a fuel reserve, a flaming pyrolysis zone, and a char reduction zone. In all the zones, the gasifier conditions show a fairly good fit between the theoretical and experimental values. In the truncated updraft condition, the heat release rate was steady in three phases: the drying phase, the flaming pyrolysis phase and the charcoal burnout. The quality of the gas was also better in the truncated updraft mode due to the cracking of tar. The flaming pyrolysis time for fuel in the gasifier is 1.6 min. The efficiency of the truncated updraft long-stick wood gasifier was found to be 79%. The gasifier designed in the present work can be implemented at pilot level in a small village at a wood consumption rate of 9 kg/h. Thus it is worked out to be 90 kg for 10 h in two batches per day. The gasifier described in the present work can furnish the need of a small village. This can operate with 3 W of blower power or other air supply to produce 1–3 kW thermal for cooking. It is simple and inexpensive to build. The gasifier will bring a litre of water to boil in 4–10 min and can be turned down to the simmer level for longer cooking and increased efficiency. With the fairly satisfactory performance and ease of construction along with the convenience of feed preparation, it is feel that the truncated updraft gasifier with long stick wood as feed would find abundant avenues of applications in a rural setting for thermal, mechanical and electrical energy delivery.

Acknowledgements

One of the authors Dr. A. Saravanakumar thanks the Ministry of New and Renewable Energy, Government of India, for financial support in the form of fellowship under the National Renewable Energy Fellowship Programme.

Nomenclature

Ag  	 Cross sectional area of the gasifier (cm2)

D 	Typical dimension (cm)

ρ 	Fuel density (g/cm3)

Fm 	Moisture content (%)

FO2 	Fraction of oxygen (%)

Fs 	Sphericity

Fv 	Void fraction

L 	Length of the wood (cm)

Lfp 	Length of the flaming pyrolysis zone (cm)

Lc 	Length of the charcoal gasification zone (cm)

M 	Mass flow rate of the fuel (kg/h)

T 	Pyrolysis zone temperature (ºC)

tfp 	Flaming pyrolysis time (s)

tc 	Char gasification time (s)

V 	Volume of the wood (cm3)

Vf 	Velocity of fuel flow (cm/s)

References

[1] 	European Commission: Energy for the future: Renewable Energy Sources-White

Paper for a Community Strategy and Action Plan. COM (97) 599, 1997, Brussels.

[2] 	International Energy Agency. World Energy Outlook 2000, IEA, Paris

[3]	Hislop D, Hall D. Biomass Resources for Gasification Plant, 1996. ETSU

B/M3/00388.

[4] 	Miles TR. Feed Preparation. Prepared for the IEA Biomass thermal Gasification

Activity 1992-1994. 1992.

[5] 	Helynen S, Hakkila P, Nousiainen I. Wood energy 1999-2003: A new national

technology programme in Finland. New Zealand Journal of Forestry Science 2000;

30:46-53.

[6] 	Saravanakumar A, Haridasan TM. Feasibility on thermal cracking of wood for

gasifier feed. In: Bioenergy - The Tenth Biennial Bio energy Conference, Boise,

Idaho. 2002.

[7] 	Cuda R, Ziak R. Gas Cleaning and Conditioning, Part 1. Theoretical Background,

Construction, Properties, Experiments,” Nordvestuysk Folkecenter for Vedvarfende

Energi, 1995, Hurup, Denmark, 32 pp.

[8] 	Bryden KM, Ragland KW. Numerical modelling of a deep, fixed bed combustor.

Energy Fuels 1996;10:269-75.

[9] 	Reed TB, Ronal Larson. Wood gas stoves for developing countries. In; Developments

in Thermochemical Biomass Conversion Conference, 1996. Canada.

[10]  Saravanakumar A, Haridasan TM, Reed TB, Kasturi Bai R. Operation and modelling

of an updraft long stick wood gasifier. Energy for Sustainable Development 2005;9:25-

39.

[11]  Saravanakumar A, Haridasan TM, Reed TB, Kasturi Bai R. Experimental

investigations of long stick wood gasification in a bottom lit updraft fixed bed

gasifier. Fuel Processing Technology 2007;88:617-22.

[12] 	Reed TB, Das A. Handbook of Biomass Gasifier Engine Systems, The Biomass

Energy Foundation Press, 1988.

[13] 	Reed TB, Graboski MS, Levie B. Fundamentals, Development and scale up of the air oxygen stratified downdraft gasifier, The Biomass Energy Foundation Press, 1988.

[14] 	Saastamoinen, J., “Sub-report. Modelling of counter flow biomass gasifiers”, 34 pp. +

Appendix, EU-project No. STEP-CT-91-0129, Gasification of waste preserved wood

impregnated with toxic inorganic and/or organic chemicals, VTT Energy, Jyvaskyla,

1994.

List of figures

Figure 1. Pilot model for truncated updraft long stick wood gasifier

Figure 2. Reactions in the truncated updraft long stick wood gasification

Figure 3. Temperature field at different zones in the gasifier

Figure 4. Air velocity Vs gas production rate

Figure 5. Diagram of 10kW truncated updraft long stick wood gasifier for thermal power

generation showing projected zone dimensions at a flaming pyrolysis time of 1.6

minutes

List of tables

Table 1. Performance of 5h and 15min run by the truncated updraft gasifier

Table 2. Results of operation of truncated updraft and conventional updraft gasifier for three

runs

Table 3. Time in flaming pyrolysis

Table 4 Theoretical and practical results for gasifier conditions

Fig. 1. Pilot model for truncated updraft long stick wood gasifier

Fig. 2. Reactions in the truncated updraft long stick wood gasification

Fig. 3. Temperature filed at different zones in the gasifier

Fig. 4. Air velocity Vs gas production rate

Fig. 5. Diagram of 10 kW truncated updraft long stick wood gasifier for thermal power

generation showing projected zone dimensions at a flaming pyrolysis time of 1.6 minutes

Table 1

Performance of 5 h and 15 min runs by the truncated updraft gasifier

| Time | Flame Temperature | Air flow rate m3/hr | Gas flow rate | Fuel Flow | Air/Fuel | MODE |
| --- | --- | --- | --- | --- | --- | --- |
| Hours | °C |  | m3/hr | kg/hr |  |  |
| 00:00 | 647 | 17 | 27 | 13 | 1.7 | Combustion |
| 00:15 | 676 | 17 | 28 | 14.3 | 1.55 | Combustion |
| 00:30 | 699 | 17 | 29 | 15.6 | 1.42 | Combustion |
| 00:45 | 715 | 17 | 30 | 16.9 | 1.31 | Combustion |
| 01:00 | 748 | 18 | 31 | 16.9 | 1.38 | Flaming Pyrolysis |
| 01:15 | 760 | 18 | 31 | 16.9 | 1.38 | Flaming Pyrolysis |
| 01:30 | 820 | 18 | 32 | 18.2 | 1.29 | Flaming Pyrolysis |
| 01:45 | 846 | 19 | 32 | 16.9 | 1.46 | Flaming Pyrolysis |
| 02:00 | 861 | 20 | 33 | 16.9 | 1.54 | Flaming Pyrolysis |
| 02:15 | 870 | 20 | 34 | 18.2 | 1.43 | Flaming Pyrolysis |
| 02:30 | 895 | 19 | 35 | 20.8 | 1.19 | Flaming Pyrolysis |
| 02:45 | 935 | 21 | 36 | 19.5 | 1.4 | Flaming Pyrolysis |
| 03:00 | 948 | 21 | 36 | 19.5 | 1.4 | Flaming Pyrolysis |
| 03:15 | 960 | 21 | 37 | 20.8 | 1.31 | Char Gasification |
| 03:30 | 984 | 22 | 38 | 20.8 | 1.38 | Char Gasification |
| 03:45 | 994 | 23 | 39 | 20.8 | 1.44 | Char Gasification |
| 04:00 | 1000 | 24 | 40 | 20.8 | 1.5 | Char Gasification |
| 04:15 | 1001 | 25 | 41 | 20.8 | 1.56 | Char Gasification |
| 04:30 | 1000 | 25 | 42 | 22.1 | 1.47 | Char Gasification |
| 04:45 | 995 | 26 | 43 | 22.1 | 1.53 | Char Gasification |
| 05:00 | 900 | 26 | 44 | 23.4 | 1.44 | Char Gasification |

Table 2

Results of operation of truncated updraft and conventional updraft gasifier for three runs

| Measured parameters | Truncated updraft | Updraft |
| --- | --- | --- |
|  | Run 1 | Run 2 | Run 3 | Run 1 | Run 2 | Run 3 |
| Moisture Content of Azadirachta wood (%) | 20 | 20 | 20 | 20 | 20 | 20 |
| Size of wood (cm) | 68 x 6 | 68 x 6 | 68 x 6 | 68 x 6 | 68 x 6 | 68 x 6 |
| Average Air Flow Rate (m3/hr) | 20.66 | 24.38 | 28.90 | 29.14 | 27 | 20.33 |
| Average Gas Flow Rate (m3/hr) | 35.14 | 37.52 | 41.47 | 37.47 | 37 | 34.91 |
| Average Gas Flame Temperature (°C) | 869 | 876 | 909 | 766 | 644 | 544 |
| Initial Fuel (kg) | 65 | 65 | 65 | 60 | 60 | 70 |
| Final Charcoal (g) | 500 | 500 | 500 | 500 | 550 | 500 |
| Particulate (g) | 0.5 | 0.3 | 0.2 | 3.5 | 1.8 | 1.7 |
| Tar (%) | 0.3 | 0.2 | 1 | 30 | 10 | 25 |
| CO (%) | 15 | 15 | 15 | 12 | 15 | 10 |
| H2 (%) | 10 | 15 | 12 | 0.02 | 0.01 | 0.03 |
| CO2 (%) | 12 | 11 | 12 | 18 | 16 | 10 |
| N2 (%) | 40 | 45 | 52 | 55 | 50 | 55 |
| Calorific value of gas (kcal / Nm3) | 4500 | 4000 | 4500 | 3000 | 3500 | 4000 |

Table 3

Time in flaming pyrolysis calculated from below equation

tfp	=   0.207 (1+1.76Fm) D (1+ 0.61D) exp (4369/RT) / (1+ 3.46Fo2) ρFsL

|  | Volume | Typical Dimen-sion | Sphericity | Density | Moisture | Temp | Oxygen Fraction | Length | Flaming Pyrolysis Time |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | V – cm3 | D (cm) | Fs | Ρ | Fm | ToC | FO2 | L | tfp-min |
| Cylindrical |  | Effect of Varying Dimensions - Azadirachta long stick wood |  |
| 6x6 | 169.6 | 5.53 | 1.8 | 0.5 | 0.20 | 600 | 0.21 | 6 | 9.018 |
| 12x5 | 235.6 | 6.17 | 1.8 | 0.5 | 0.20 | 600 | 0.21 | 12 | 5.480 |
| 24x6 | 678.5 | 8.77 | 1.8 | 0.5 | 0.20 | 600 | 0.21 | 24 | 5.196 |
| 68x5 | 1335.0 | 10.98 | 1.8 | 0.5 | 0.20 | 600 | 0.21 | 68 | 2.787 |
| 68x6 | 1922.6 | 12.40 | 1.8 | 0.5 | 0.20 | 600 | 0.21 | 68 | 3.500 |
|  |  | Effect of Varying Temperature - 68 cm Azadirachta long stick wood |  |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 650 | 0.21 | 68 | 2.429 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 700 | 0.21 | 68 | 2.149 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 750 | 0.21 | 68 | 1.924 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 800 | 0.21 | 68 | 1.741 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 850 | 0.21 | 68 | 1.589 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 900 | 0.21 | 68 | 1.462 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 950 | 0.21 | 68 | 1.354 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.20 | 1000 | 0.21 | 68 | 1.262 |
|  |  | Effect of Varying Moisture - 68 cm Azadirachta long stick wood |  |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.1 | 1000 | 0.21 | 68 | 1.097 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.2 | 1000 | 0.21 | 68 | 1.262 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.3 | 1000 | 0.21 | 68 | 1.344 |
| 68x6 | 1922 | 12.4 | 1.8 | 0.5 | 0.4 | 1000 | 0.21 | 68 | 1.508 |
|  |  | Effect of Varying Density – 68 cm selected species |  |  |
| Azadirachta | 1922 | 12.4 | 1.8 | 0.52 | 0.20 | 800 | 0.21 | 68 | 1.674 |
| Acacia | 1922 | 12.4 | 1.8 | 0.59 | 0.20 | 800 | 0.21 | 68 | 1.475 |
| Casuarina | 1922 | 12.4 | 1.8 | 0.67 | 0.20 | 800 | 0.21 | 68 | 1.299 |
| Eucalyptus | 1922 | 12.4 | 1.8 | 0.74 | 0.20 | 800 | 0.21 | 68 | 1.176 |
|  |  | Effect of Varying Spericity - Various shape Azadirachta |  |  |
| 68x2 | 1335 | 10.98 | 0.73 | 0.5 | 0.20 | 900 | 0.21 | 68 | 3.604 |
| 68x3 | 1335 | 10.98 | 1.1 | 0.5 | 0.20 | 900 | 0.21 | 68 | 2.392 |
| 68x4 | 1335 | 10.98 | 1.5 | 0.5 | 0.20 | 900 | 0.21 | 68 | 1.754 |
| 68x5 | 1335 | 10.98 | 1.8 | 0.5 | 0.20 | 900 | 0.21 | 68 | 1.462 |
| 68x6 | 1335 | 10.98 | 2.28 | 0.5 | 0.20 | 900 | 0.21 | 68 | 1.154 |

Table 4

Theoretical and practical results for gasifier conditions

| Gasifier conditions | Theoretical results | Practical results |
| --- | --- | --- |
| Pyrolysis temperature (T) | 850 | 850 |
| Pyrolysis zone Pyrolysis time (tfp) Fuel velocity (Vf) Pyrolysis zone length (Lfp) | 96sec 0.3m/sec 34.2cm | 104sec 38cm |
| Char gasification zone Char gasification time (tc) Char gasification length (Lc) | 100sec 30cm | 100 sec 35cm |
| Total gasifier active length Fuel transit time (tfp + tc) Active zone length (Lfp + Lc) | 196sec 64.2cm | 210sec 73cm |